## Slide 1: Machine-Level Programming II: Control
Carnegie Mellon
Carnegie Mellon
Slides adapted from Bryant and O’Hallaron

## Slide 2: What have we learnt so far
Abstract view of machine
  CPU (CPU state: registers, conditional codes, %RIP)
  Memory
ISA is an API to hardware
Example instructions:
  MOV: move data between CPU/memory
  Arithmetic (ADD, SUB)
  LEA
  Various addressing modes: mov %rax, 0x8(%rdx)
  No instructions operate on two memory operands

## Slide 3: Today: How control flow is done
Carnegie Mellon
Condition codes
Conditional branches
Loops
Switch Statements

## Slide 4: Processor State (x86-64)
Carnegie Mellon
Registers
Condition codes (single bit registers)
%rip
CF
ZF
SF
OF
%rsp
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp

## Slide 5: Condition Codes (implicit setting)
Carnegie Mellon
Implicitly set by arithmetic operations
  Example: addq Src, Dest  t = a + b
  CF (Carry Flag) set if unsigned overflow
  ZF (Zero Flag) set if t == 0
  SF (Sign Flag) set if t < 0 (as signed)
  OF (OverFlow Flag) set if signed overflow (a>0 && b>0 && t<0) || (a<0 && b<0 && t>=0)
Not set by leaq
Examples:
  a=0xff...ff b=0x00....01
  a=0x80...00 b=0xff....ff
Notes: a = 0xffff...ff
b = 0x00....1
What are the flags set?
CF
ZF
a = 0x800...0
b = 0xfff.... fff
What are the flags set?
CF
OF

## Slide 6: Condition Codes (Explicit Setting: Compare)
Carnegie Mellon
Explicit set by Compare Instruction
  cmpq b,a like computing a-b without setting destination
  CF set if unsigned overflow
  ZF set if a == b
  SF set if (a-b) < 0 (as signed)
  OF set if two’s-complement (signed) overflow (a>=0 && b<0 && (a-b)<0) || (a<0 && b>0 && (a-b)>0)
Examples:
  cmpq $0x10, %rax (Give an example value of %rax such that CF/ZF/SF/OF set?)
Notes: CF: %rax < 10 0xffff.... (not set)
ZF: %rax == 10
SF: %rax < 0 || %rax < 10
OF: %rax = 0x80000...

## Slide 7: Condition Codes (Explicit Setting: Test)
Carnegie Mellon
Explicit set by Test instruction
  testq b, a (like computing a&b without setting destination)
  ZF set when a&b == 0
  SF set when a&b < 0
Examples:
  testq %rax, %rax (when is ZF/SF set?)

## Slide 8: Reading Condition Codes
Carnegie Mellon
SetX Instructions
  Set low-order byte of destination register to 0/1 based on condition codes
  Does not alter remaining 7 bytes
SetX | Condition | Description
sete | ZF | Equal / Zero
setne | ~ZF | Not Equal / Not Zero
sets | SF | Negative
setns | ~SF | Nonnegative
setg | ~(SF^OF)&~ZF | Greater (Signed)
setge | ~(SF^OF) | Greater or Equal (Signed)
setl | (SF^OF) | Less (Signed)
setle | (SF^OF)¦ZF | Less or Equal (Signed)
seta | ~CF&~ZF | Above (unsigned)
setb | CF | Below (unsigned)
cmpq %rbx, %rax
setl %al
SF=1 OF=0
%rbx > %rax
SF=0 OF=1
 %rax<0, %rbx > 0

## Slide 9: x86-64 Integer Registers
%rsp
%bl
%cl
%dl
%sil
%dil
%spl
%bpl
%r8b
%r9b
%r10b
%r11b
%r12b
%r13b
%r14b
%r15b
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%eax
%rsi
%rdi
%rbp
%al

## Slide 10: Reading Condition Codes (Cont.)
cmpq %rsi, %rdi # Compare x:y
  setg %al # Set when >
  movzbl %al, %eax # Zero rest of %eax
ret
Carnegie Mellon
SetX Example:
int gt (long x, long y)
{
return x > y;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%eax | Return value

## Slide 11: Today
Carnegie Mellon
Control: Condition codes
If statements
While and For loops

## Slide 12: Jumping
Carnegie Mellon
jX Instructions: jump to different part of code
jX | Condition | Description
jmp | 1 | Unconditional
je | ZF | Equal / Zero
jne | ~ZF | Not Equal / Not Zero
js | SF | Negative
jns | ~SF | Nonnegative
jg | ~(SF^OF)&~ZF | Greater (Signed)
jge | ~(SF^OF) | Greater or Equal (Signed)
jl | (SF^OF) | Less (Signed)
jle | (SF^OF)¦ZF | Less or Equal (Signed)
ja | ~CF&~ZF | Above (unsigned)
jb | CF | Below (unsigned)

## Slide 13: Conditional Branch Example
Carnegie Mellon
long compare
(long x, long y)
{
long result;
if (x > 10*y)
result = 1;
else
result = 0;
return result;
}
compare:
leaq (%rsi,%rsi,4), %rax
addq %rax, %rax
cmpq %rdi, %rax
jge .L3
movl $1, %eax
ret
.L3:
movl $0, %eax
ret
gcc –Og –S compare.c
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value
10*y-x

## Slide 14: Equivalent goto code
Carnegie Mellon
long compare
(long x, long y)
{
long result;
if (x > 10*y)
result = 1;
else
result = 0;
return result;
}
Machine code is essentially doing control flow with goto statement
long absdiff_j (long x, long y)
{
long result;
int ntest = 10*y-x;
if (ntest >= 0) goto Else;
result = 1;
return result;
Else:
result = 0;
Done:
return result;
}
Do not write this normally

## Slide 15: Today
Carnegie Mellon
Control: Condition codes
If statements
Loops
Switch Statements

## Slide 16: “While” Translation #1
Carnegie Mellon
While version
while (Test)
Body
“Jump-to-middle” translation
Used with -Og
Goto Version
goto test;
loop:
Body
test:
if (Test)
goto loop;

## Slide 17: “While” Translation example #1
Carnegie Mellon
long log_2(unsigned long x)
{
long log = 0;
while (x != 0) {
x = x >> 1;
log++;
}
return log;
}
log_2:
movl $0, %eax
jmp .L2
.L3:
shrq %rdi
addq $1, %rax
.L2:
testq %rdi, %rdi
jne .L3
ret
gcc –Og –S log_2.c
Register | Use(s)
%rdi | Argument x
%rax | Return value
right shift, zero fill

## Slide 18: “While” Translation #2
Carnegie Mellon
While version
while (Test)
Body
Do-While Version
if (!Test)
goto done;
do
Body
while(Test);
done:
Used with –O1 –O2
Why?
  allows optimization of initial condition
Goto Version
if (!Test)
goto done;
loop:
Body
if (Test)
goto loop;
done:

## Slide 19: “While” Translation example #2
Carnegie Mellon
long log_2(unsigned long x)
{
long log = 0;
while (x != 0) {
x = x >> 1;
log++;
}
return log;
}
log_2:
testq %rdi, %rdi
je .L4
movl $0, %eax
.L3:
shrq %rdi
addq $1, %rax
testq %rdi, %rdi
jne .L3
ret
.L4:
movl $0, %eax
ret
gcc –O1 –S log_2.c
Register | Use(s)
%rdi | Argument x
%rax | Return value

## Slide 20: “For” Loop translation
Carnegie Mellon
for (Init; Test; Update )
Body
For Version
Init;
while (Test ) {
Body
Update;
}
While Version

## Slide 21: “Loop” Translation example
Carnegie Mellon
int sum(int n)
{
int sum = 0;
for (int i=0; i<n; i++){
sum += i;
}
return sum;
}
sum:
movl $0, %edx
movl $0, %eax
jmp .L5
.L6:
addl %edx, %eax
addl $1, %edx
.L5:
cmpl %edi, %edx
jl .L6
rep ret
gcc –Og –S log_2.c
Register | Use(s)
%rdi | Argument x
%rax | Return value

## Slide 22: Summary
Carnegie Mellon
Today
  Control: Condition codes
  If statements
  While and for statements
Not discussed
  Switch statements

## Slide 23: Binary Puzzle
mystery:
movl $0, %edx
movl $0, %eax
movl $1, %ecx
jmp .L8
.L10:
testl %ecx, %edi
je .L9
addl $1, %eax
.L9:
addl %ecx, %ecx
addl $1, %edx
.L8:
cmpl $31, %edx
jle .L10
ret
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value
Function signature?
  one, two or more parameters? type?
  return type?
Is there a loop? What’s termination condition?