## Slide 1: Machine-Level Programming V: Buffer overflow
Slides adapted from Bryant and O’Hallaron

## Slide 2: Recall: Memory Referencing Bug Example
Carnegie Mellon
fun(0) ➙ 3.14
fun(1) ➙ 3.14
fun(2) ➙ 3.1399998664856
fun(3) ➙ 2.00000061035156
fun(4) ➙ 3.14
fun(6) ➙ Segmentation fault
typedef struct {
int a[2];
double d;
} struct_t;
double fun(int i) {
volatile struct_t s;
s.d = 3.14;
s.a[i] = 1073741824;
return s.d;
}
Critical State | 
? | 
? | 
d7 ... d4 | 
d3 ... d0 | 
a[1] | 
a[0] | 
struct_t
s.a[2]
s.a[3]
s.a[4]
s.a[5]
s.a[6]

## Slide 3: Such problems are a BIG deal
Generally called a “buffer overflow”
  when exceeding the memory size allocated for an array
#1 technical cause of security vulnerabilities
Most common form
  Unchecked lengths on string inputs
  Particularly for bounded character arrays on the stack

## Slide 4: Bad APIs of stdlib make buffer overflow likely
E.g. gets()
  No way to specify limit on number of characters to read
Other examples: strcpy, strcat, scanf, fscanf, sscanf
/* Get string from stdin */
char *gets(char *dest) { int c = getchar();
char *p = dest;
while (c != EOF && c != '\n') {
*p++ = c;
c = getchar();
}
*p = '\0';
return dest;
}

## Slide 5: Vulnerable Buffer Code
void call_echo() {
echo();
}
/* Echo Line */ void echo() { char buf[4]; /* Way too small! */ gets(buf); puts(buf); }
unix>./a.out
Type a string:012345678901234567890123
012345678901234567890123
unix>./a.out
Type a string:0123456789012345678901234
Segmentation Fault
how big
is big enough?

## Slide 6: Buffer Overflow Disassembly
00000000004006cf <echo>:
4006cf: 48 83 ec 18 sub $0x18,%rsp
4006d3: 48 89 e7 mov %rsp,%rdi
4006d6: e8 a5 ff ff ff callq 400680 <gets>
4006db: 48 89 e7 mov %rsp,%rdi
4006de: e8 3d fe ff ff callq 400520 <puts@plt>
4006e3: 48 83 c4 18 add $0x18,%rsp
4006e7: c3 retq
4006e8: 48 83 ec 08 sub $0x8,%rsp
4006ec: b8 00 00 00 00 mov $0x0,%eax
4006f1: e8 d9 ff ff ff callq 4006cf <echo>
4006f6: 48 83 c4 08 add $0x8,%rsp
4006fa: c3 retq
call_echo:
echo:

## Slide 7: Buffer Overflow Stack
echo:
subq $24, %rsp
movq %rsp, %rdi
call gets
. . .
/* Echo Line */ void echo() { char buf[4]; /* Way too small! */ gets(buf); puts(buf); }
Return Address
(8 bytes)
%rsp
Stack Frame
for call_echo
[3]
[2]
[1]
[0]
buf
Before call to gets
20 bytes unused

## Slide 8: Buffer Overflow Stack Example
echo:
subq $24, %rsp
movq %rsp, %rdi
call gets
. . .
void echo() { char buf[4];
gets(buf); . . . }
Return Address
(8 bytes)
%rsp
Stack Frame
for call_echo
[3]
[2]
[1]
[0]
buf
Before call to gets
20 bytes unused
. . .
4006f1: callq 4006cf <echo>
4006f6: add $0x8,%rsp
. . .
call_echo:
00
40
06
f6
00
00
00
00

## Slide 9: Buffer Overflow Stack Example #1
echo:
subq $24, %rsp
movq %rsp, %rdi
call gets
. . .
void echo() { char buf[4];
gets(buf); . . . }
Return Address
(8 bytes)
%rsp
Stack Frame
for call_echo
33
32
31
30
buf
After call to gets
20 bytes unused
. . .
4006f1: callq 4006cf <echo>
4006f6: add $0x8,%rsp
. . .
call_echo:
00
40
06
f6
00
00
00
00
unix>./bufdemo-nsp
Type a string:01234567890123456789012
01234567890123456789012
37
36
35
34
31
30
39
38
35
34
33
32
39
38
37
36
00
32
31
30
Overflowed buffer, but did not corrupt state

## Slide 10: Buffer Overflow Stack Example #2
echo:
subq $24, %rsp
movq %rsp, %rdi
call gets
. . .
void echo() { char buf[4];
gets(buf); . . . }
Return Address
(8 bytes)
%rsp
Stack Frame
for call_echo
33
32
31
30
buf
After call to gets
20 bytes unused
. . .
4006f1: callq 4006cf <echo>
4006f6: add $0x8,%rsp
. . .
call_echo:
00
00
00
00
unix>./bufdemo-nsp
Type a string:0123456789012345678901234
Segmentation Fault
37
36
35
34
31
30
39
38
35
34
33
32
39
38
37
36
33
32
31
30
Overflowed buffer and corrupted return pointer
00
40
00
34

## Slide 11: Buffer Overflow Stack Example #3
echo:
subq $24, %rsp
movq %rsp, %rdi
call gets
. . .
void echo() { char buf[4];
gets(buf); . . . }
Return Address
(8 bytes)
%rsp
Stack Frame
for call_echo
33
32
31
30
buf
After call to gets
20 bytes unused
. . .
4006f1: callq 4006cf <echo>
4006f6: add $0x8,%rsp
. . .
call_echo:
00
00
00
00
unix>./bufdemo-nsp
Type a string:012345678901234567890123
012345678901234567890123
37
36
35
34
31
30
39
38
35
34
33
32
39
38
37
36
33
32
31
30
Overflowed buffer, corrupted return pointer, but program seems to work!
00
40
06
00

## Slide 12: Buffer Overflow Stack Example #3 Explained
Return Address
(8 bytes)
%rsp
Stack Frame
for call_echo
33
32
31
30
buf
After call to gets
20 bytes unused
. . .
400600: mov %rsp,%rbp
400603: mov %rax,%rdx
400606: shr $0x3f,%rdx
40060a: add %rdx,%rax
40060d: sar %rax
400610: jne 400614
400612: pop %rbp
400613: retq
register_tm_clones:
00
00
00
00
37
36
35
34
31
30
39
38
35
34
33
32
39
38
37
36
33
32
31
30
“Returns” to unrelated code
Lots of things happen, without modifying critical state
Eventually executes retq back to main
00
40
06
00

## Slide 13: What’s the big deal about buffer overflow?
How does attackers take advantage of this bug?
  overwrite with a carefully chosen return address
  executes malicious code (injected by attacker or elsewhere in the running process)
What can attackers do once they are executing code?
  To gain easier access, e.g. execute a shell
  Take advantage of the permissions granted to the hacked process
    if the process is running as “root”....
    read user database, send spam etc.
//webserver code
void read_user_request() { char buf[200];
gets(buf); ...
}
Systems software is often written in C:
  operating system, file systems, database, compilers, network servers, command shells, ...

## Slide 14: Example exploit: Code Injection Attacks
Input string contains byte representation of executable code
Overwrite return address A with address of buffer B
When Q executes ret, will jump to exploit code
int Q() {
char buf[64];
gets(buf);
...
return ...;
}
void P(){
Q();
...
}
return
address
A
Stack after call to gets()
B
P stack frame
Q stack frame
B
exploit
code
pad
data written
by gets()

## Slide 15: Exploits Based on Buffer Overflows
Buffer overflow bugs can allow remote machines to execute arbitrary code on victim machines
Common in real progams
Examples across the decades
  “Internet worm” (1988)
  Attacks on Xbox
  Jaibreaks on iPhone
  …
Recent measures make these attacks much more difficult

## Slide 16: Example: the original Internet worm (1988)
Exploited a few vulnerabilities to spread
  Early finger server (fingerd) used gets() to read client inputs:
    finger sexton@nyu.edu
  Worm attacked fingerd server by sending phony argument:
    finger “exploit-code padding new-return-address”
    exploit code: executed a root shell on the victim machine with a direct TCP connection to the attacker.
Once on a machine, scanned for other machines to attack
  invaded ~6000 computers in hours (10% of the Internet  )
    see June 1989 article in Comm. of the ACM
  the young author of the worm was prosecuted…

## Slide 17: OK, what to do about buffer overflow attacks
Write correct code: avoid overflow vulnerabilities
Mitigate attack despite buggy code

## Slide 18: Avoid Overflow Vulnerabilities in Code
Better coding practices
  e.g. use library routines that limit string lengths, fgets instead of gets, strncpy instead of strcpy
Use a memory-safe language instead of C
bug finding tools?
/* Echo Line */ void echo() { char buf[4]; /* Way too small! */ fgets(buf, 4, stdin); puts(buf); }

## Slide 19: Mitigate BO attacks despite buggy code
A buffer overflow attack typically needs two components:
  Control-flow hijacking
    overwrite a code pointer (e.g. return address) that’s later invoked
  Need some interesting code in the process’ memory
    e.g. put code in the buffer
    Process already contains a lot of code in predictable location
How to mitigate attacks? make #1 or #2 hard

## Slide 20: Mitigate #1 (control flow hijacking)
Idea: Catch over-written return address before invocation!
  Place special value (“canary”) on stack just beyond buffer
  Check for corruption before exiting function
GCC Implementation
  -fstack-protector
  Now the default
unix>./bufdemo-sp
Type a string:0123456
0123456
unix>./bufdemo-sp
Type a string:01234567
*** stack smashing detected ***

## Slide 21: Setting Up Canary
/* Echo Line */ void echo() { char buf[4]; gets(buf); puts(buf); }
Return Address
(8 bytes)
%rsp
Stack Frame
for call_echo
[3]
[2]
[1]
[0]
buf
Before call to gets
Canary
(8 bytes)
Where should canary go?
When should canary checking happen?
What should canary contain?

## Slide 22: Stack canaries
40072f: sub $0x18,%rsp
400733: mov %fs:0x28,%rax
40073c: mov %rax,0x8(%rsp)
400741: xor %eax,%eax
400743: mov %rsp,%rdi
400746: callq 4006e0 <gets>
40074b: mov %rsp,%rdi
40074e: callq 400570 <puts@plt>
400753: mov 0x8(%rsp),%rax
400758: xor %fs:0x28,%rax
400761: je 400768 <echo+0x39>
400763: callq 400580 <__stack_chk_fail@plt>
400768: add $0x18,%rsp
40076c: retq
echo:

## Slide 23: Setting Up Canary
echo:
. . .
movq %fs:40, %rax # Get canary
movq %rax, 8(%rsp) # Place on stack
xorl %eax, %eax # Erase canary
. . .
/* Echo Line */ void echo() { char buf[4]; gets(buf); puts(buf); }
Return Address
(8 bytes)
%rsp
Stack Frame
for call_echo
[3]
[2]
[1]
[0]
buf
Before call to gets
Canary
(8 bytes)

## Slide 24: Checking Canary
echo:
. . .
movq 8(%rsp), %rax # Retrieve from stack
xorq %fs:40, %rax # Compare to canary
je .L6 # If same, OK
call __stack_chk_fail # FAIL
.L6: . . .
/* Echo Line */ void echo() { char buf[4];
gets(buf); puts(buf); }
Return Address
Saved %ebp
Stack Frame
for main
[3]
[2]
[1]
[0]
Before call to gets
Saved %ebx
Canary
Return Address
(8 bytes)
%rsp
Stack Frame
for call_echo
33
32
31
30
buf
After call to gets
20 bytes unused
Canary
(8 bytes)
00
36
35
34
Input: 0123456

## Slide 25: What isn’t caught by canaries?
Overwrite a code pointer before canary
Overwrite a data pointer before canary
void myFunc(char *s) {
...
}
void echo() { void (*f)(char *);
f = myFunc;
char buf[8];
gets(buf);
f();
}
void echo() { long *ptr;
char buf[8];
gets(buf);
*ptr = *(long *)buf;
}

## Slide 26: Mitigate #2 attempts to craft “attacking code” (NX)
NX: Non-executable code segments
  Traditional x86 has no “executable” permission bit, X86-64 added explicit “execute” permission
  Stack marked as non-executable
Does not defend against:
  Modify return address to point to code in stdlib (which has functions to execute any programs e.g. shell)
Stack after call to gets()
B
P stack frame
Q stack frame
B
exploit
code
pad
data written
by gets()
Any attempt to execute this code will fail

## Slide 27: Mitigate #2 attempts to craft “attacking code” (ASLR)
Insight: attacks often use hard-coded address  make it difficult for attackers to figure out the address to use
Address Space Layout Randomization
  Stack randomization
    Makes it difficult to determine where the return addresses are located
  Randomize the heap, location of dynamically loaded libraries etc.

## Slide 28: The rest of the slides are optional

## Slide 29: Return-Oriented Programming Attacks
Challenge (for hackers)
  Stack randomization makes it hard to predict buffer location
  Non-executable stack makes it hard to insert arbitrary binary code
Alternative Strategy
  Use existing code
    E.g., library code from stdlib
  String together fragments to achieve overall desired outcome
  Does not overcome stack canaries
How to concoct an arbitrary mix of instructions from the current running program?
  Gadgets: Sequence of instructions ending in ret
    Encoded by single byte 0xc3
  Code positions fixed from run to run
  Code is executable

## Slide 30: Gadget Example #1
Use tail end of existing functions
long ab_plus_c
(long a, long b, long c) {
return a*b + c;
}
00000000004004d0 <ab_plus_c>:
4004d0: 48 0f af fe imul %rsi,%rdi
4004d4: 48 8d 04 17 lea (%rdi,%rdx,1),%rax
4004d8: c3 retq
rax  rdi + rdx
Gadget address = 0x4004d4

## Slide 31: Gadget Example #2
Repurpose byte codes
void setval(unsigned *p) {
*p = 3347663060u;
}
<setval>:
4004d9: c7 07 d4 48 89 c7 movl $0xc78948d4,(%rdi)
4004df: c3 retq
rdi  rax
Gadget address = 0x4004dc
Encodes movq %rax, %rdi

## Slide 32: ROP Execution
Trigger with ret instruction
  Will start executing Gadget 1
Final ret in each gadget will start next one



c3
Gadget 1 code
c3
Gadget 2 code
c3
Gadget n code
Stack
%rsp