## Slide 1: Machine-Level Programming III: How to implement procedure calls Jinyang Li
Carnegie Mellon
Slides adapted from Bryant and O’Hallaron

## Slide 2: Requirements of procedure calls?
Passing control
Passing Arguments & return value
Allocate / deallocate local variables
P(…) {
•
•
y = Q(x);
y++;
•
}
int Q(int i)
{
int t, z;
..
..
return z;
}

## Slide 3: How to transfer control for procedure calls?
Carnegie Mellon
void main(){
..
f(..)
L1: ..
}
void f(){
..
g(..)
L2: ..
}
void g(){
..
h(..)
L3: ..
}
Jump to f()
Remember where to come back
L1
Jump to g()
Remember where to come back
L2
L1
Jump to h()
Remember where to come back
L3
L2
L1

## Slide 4: How to transfer control for procedure calls?
Carnegie Mellon
void main(){
..
f(..)
L1: ..
}
void f(){
..
g(..)
L2: ..
}
void g(){
..
h(..)
L3: ..
}
Jump to L1
Forget L1
Jump to L2
Forget L2
Jump to L3
Forget L3
L3
L2
L1

## Slide 5: x86-64 Stack
Region of memory managed like a stack
Grows toward lower addresses
Register %rsp contains lowest stack address
  address of “top” element
Stack Pointer: %rsp
Stack Grows
Down
Increasing
Addresses
Stack “Top”
Stack “Bottom”

## Slide 6: Push instruction
Carnegie Mellon
pushq Src
  fetch operand src
  Decrement %rsp by 8
  Write operand at address given by %rsp
-8
Stack Grows
Down
Increasing
Addresses
Stack “Bottom”
Stack Pointer: %rsp
Stack “Top”

## Slide 7: Pop instruction
Stack Pointer: %rsp
Stack Grows
Down
Increasing
Addresses
Stack “Top”
Stack “Bottom”
Carnegie Mellon
+8
popq Dest
  Read value at address given by %rsp
  Increment %rsp by 8
  Store value at Dest (must be register)

## Slide 8: Call and Ret instructions
Carnegie Mellon
call label
  Push return address on stack
  Jump to label
ret
  Pop 8 bytes (address) from stack
  Jump to address
Next instrution after the call instruction

## Slide 9: Using the stack
Carnegie Mellon
void main(){
..
f(..)
L1: ..
}
void f(){
..
g(..)
L2: ..
}
void g(){
..
}
Jump to L3
Remember where to come back
Jump to L5
Remember where to come back
L2
L1
Call L3
L3:
Call L5
L5:

## Slide 10: Using the stack
Carnegie Mellon
void main(){
..
f(..)
L1: ..
}
void f(){
..
g(..)
L2: ..
}
void g(){
..
}
Pop L1 from stack
Jump to L1
Pop L2 from stack
Jump to L2
L2
L1
Call L3
L3:
Call L5
L5:
ret
ret

## Slide 11: Control Flow Example #1
0000000000400550 <func>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <main>:
•
•
400544: callq 400550 <func>
400549: mov %rax,(%rbx)
•
•
0x400544
0x120
•
•
•
%rsp
0x120
0x128
0x130
%rip

## Slide 12: Control Flow Example #2
0000000000400550 <mult2>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <multstore>:
•
•
400544: callq 400550 <mult2>
400549: mov %rax,(%rbx)
•
•
0x400550
0x118
0x400549
•
•
•
%rsp
0x120
0x128
0x130
0x118
%rip

## Slide 13: Control Flow Example #3
0000000000400550 <mult2>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <multstore>:
•
•
400544: callq 400550 <mult2>
400549: mov %rax,(%rbx)
•
•
0x400557
0x118
0x400549
•
•
•
%rsp
0x120
0x128
0x130
0x118
%rip

## Slide 14: Control Flow Example #4
0000000000400550 <mult2>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <multstore>:
•
•
400544: callq 400550 <mult2>
400549: mov %rax,(%rbx)
•
•
0x400549
0x120
•
•
•
%rsp
0x120
0x128
0x130
%rip
0x400549

## Slide 15: How to allocate/deallocate local variables?
Use registers whenever possible
Allocate local variables on the stack
  subq $0x8,%rsp //allocate 8 bytes
  movq $1, 8(%rsp) //store 1 in the allocated 8 bytes
De-allocate then from the stack before returning
  addq $0x8,%rsp

## Slide 16: How to pass arguments and return values?
We could store arguments/return values on the stack
  Not very efficient
C tries to pass arguments and return values using registers
  C’s calling convention

## Slide 17: C’s calling convention: args/return values
Registers
First 6 arguments
Return value
Stack
Only allocate stack space when needed
%rdi
%rsi
%rdx
%rcx
%r8
%r9
%rax
Arg 7
• • •
Arg 8
Arg n
• • •

## Slide 18: What does mystery function do?
Carnegie Mellon
<mystery>:
movq (%rdi), %rax
addq $1, %rax
movq %rax, (%rdi)
ret
…
leaq 8(%rsp), %rdi
call <mystery>
…
void mystery(long *x) {
(*x)++;
}

## Slide 19: Calling convention: Register Saving
Carnegie Mellon
When procedure f calls g:
  f is the caller, g is the callee
Can caller assume register values do not change when callee returns?
If not, caller must save register values (in memory) that it needs to use them later

## Slide 20: Calling convention: register saving
Carnegie Mellon
Some registers are “caller saved”, others are “callee saved”
  Caller saved
    Caller saves “caller saved” registers on stack before the call
  Callee saved
    Callee saves “callee saved” registers on stack before using
    Callee restores them before returning to caller

## Slide 21: C’ calling convention: Register Usage
%rax
%rdx
%rcx
Return value
%r8
%r9
%r10
%r11
%rdi
%rsi
Arguments
Caller-saved
%rbx
%rsp
Callee-saved
%rbp
%r12
%r13
%r14

## Slide 22: Why caller vs. callee saved registers?
Carnegie Mellon
Why not make all registers caller saved?
Why not make all registers callee saved?

## Slide 23: Register save Example
Carnegie Mellon
func:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
%rsp
Initial Stack Structure
. . .
Rtn address
15213
Unused
%rsp
Resulting Stack Structure
. . .
Rtn address
%rsp+8
Saved %rbx
long func(long x) {
long v1 = 15213;
long v2 = incr(&v1);
return x+v2;
}

## Slide 24: Register save example
Carnegie Mellon
func:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long func(long x) {
long v1 = 15213;
long v2 = incr(&v1);
return x+v2;
}
%rsp
Pre-return Stack Structure
. . .
Rtn address
15213
Unused
%rsp
Resulting Stack Structure
. . .
Rtn address
%rsp+8
Saved %rbx

## Slide 25: Stack Frames
We view the part of stack pertaining to each function invocation as a “stack frame”

## Slide 26: x86-64/C Stack Frame
Carnegie Mellon
Current Stack Frame (“Top” to Bottom)
  “Argument build:” Parameters for function about to call
  Local variables (if can’t be kept in registers)
  Saved register context
Caller Stack Frame
  Return address
    Pushed by call instruction
  Arguments for this call
Return Addr
Saved
Registers
+
Local
Variables
Argument
Build
(Optional)
Arguments
7+
Caller
Frame
Stack pointer
%rsp

## Slide 27: Example
Carnegie Mellon
yoo
who
amI
amI
amI
amI
yoo
%rsp
Stack
yoo
yoo(…)
{
•
•
who();
•
•
}

## Slide 28: Example
yoo(…)
{
•
•
who();
•
•
}
Carnegie Mellon
yoo
who
amI
amI
amI
amI
yoo
%rsp
Stack
yoo
who
who(…)
{
• • •
amI();
• • •
amI();
• • •
}

## Slide 29: Example
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
Carnegie Mellon
yoo
who
amI
amI
amI
amI
yoo
%rsp
Stack
yoo
who
amI
amI(…)
{
•
•
amI();
•
•
}

## Slide 30: Example
Carnegie Mellon
yoo
who
amI
amI
amI
yoo
%rsp
Stack
yoo
who
amI
amI
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}
amI(…)
{
•
•
amI();
•
•
}

## Slide 31: Example
Carnegie Mellon
yoo
who
amI
amI
amI
yoo
%rsp
Stack
yoo
who
amI
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}

## Slide 32: Example
Carnegie Mellon
yoo
who
amI
amI
amI
amI
yoo
%rsp
Stack
yoo
who
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}

## Slide 33: Example
Carnegie Mellon
yoo
who
amI
amI
amI
amI
yoo
%rsp
Stack
yoo
who
amI
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}

## Slide 34: Example
Carnegie Mellon
yoo
who
amI
amI
amI
amI
yoo
%rsp
Stack
yoo
who
yoo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}

## Slide 35: Example
Carnegie Mellon
yoo
who
amI
amI
amI
amI
yoo
%rsp
Stack
yoo
yoo(…)
{
•
•
who();
•
•
}

## Slide 36: C/x86-64 Procedure Summary
Carnegie Mellon
Uses stack for procedure call / return
Content of stack frame:
  Local variables
  Saved registers
  Arguments
  Return address
Return Addr
Saved
Registers
+
Local
Variables
Argument
Build
Old %rbp
Arguments
7+
Caller
Frame
%rbp
(Optional)
%rsp